## Slide 1: CS 2261 Recitation 6 1/30
Basic Animation, Multiple files, and Flicker

## Slide 2: Announcements and Clarifications
Lab01 grades are out
HW01 due Thursday (2/1)
HW02 released tonight, due next Tuesday (2/6)

## Slide 3: Basic Animation

## Slide 4: Introduction
There’s no such thing as magic.
  You tell the pixels what to be, and they do that until told otherwise
Remember these?
  https://youtu.be/EQG8eZs8AJc
In works just like that
  Draw, erase, then draw again
Be efficient
  Don’t erase or draw unless you need to

## Slide 5: Slowing it down
There’s no such thing as magic.
  You told it what to do, and it’ll do it as fast as possible
Give it some work to do between frames
  void delay(int amount) {
  int trash = 0;
  for(int i=0; i<amount*1000; i++) {
  trash++;
  }
  }
This won’t delay anything (not even a little bit)

## Slide 6: C thinks it’s smarter than you
You (usually) want your code to run as fast as possible.
C will not even compile sections that aren’t doing anything
  Like incrementing an unused variable
Solution: the keyword volatile
  It means “Shut up C, I know what I’m doing.”
  Doesn’t allow the compiler to optimize, so don’t abuse it
  void delay(int amount) {
  volatile int trash = 0;
  for(int i=0; i<amount*1000; i++) {
  trash++;
  }
  }

## Slide 7: Animating moving objects
Draw, then delay, erase, draw, repeat.
  Or, better: erase, draw, delay, repeat.
Find a balance of movement speed (pixels per frame) and delay
  speed delay: too slow
  speed delay: too fast
  speed delay: flicker
  speed delay: “low framerate”

## Slide 8: Moving objects with code
Just like animating
  Delay, erase, draw, repeat
Put the erase-draw-delay cycle into a loop
Make the drawing parameters into variables
Manipulate the variables as you see fit
It’s not rocket science; it’s computer science.

## Slide 9: Multiple Files

## Slide 10: Introduction
Our main files are getting big…
  …and they’re just gonna keep growing
We need better code organization
  Every game may need setPixel, but won’t need code specific to another game

## Slide 11: Introducing myLib.c
It would benefit us to make a “library file” with reusable code
  COLOR macros, OFFSET, setPixel, delay, videoBuffer, etc.
  Not main, movePlayerLeft, isGameOver, etc.
Make sure to add it to your Makefile SOURCES
  Otherwise make won’t know it exists
How will main.c know it exists?
  To call drawRect, it needs to know what drawRect needs to know.

## Slide 12: Header Files
A special type of file that only the preprocessor cares about
You can put preprocessor things and declarations in them
  But no memory-affecting code (assignments, function definitions, etc.)
For myLib.c, create myLib.h and copy that stuff in
  And remove them from myLib.c after copying
At the top of myLib.c, add: #include “myLib.h”
  Do the same for every .c file that needs the macros, variable declarations, and functions whose prototypes are in myLib.h
Our Makefile doesn’t need to know

## Slide 13: Including Header Files
At the top of each file that needs it
  #include “headerFileName.h”
There are also C libraries included with your C distribution
  stdlib (java.util), stdio (java.io), etc.
Include their header files to access the functions and other goodies they provide
  #include <stdlib.h>
  Uses <> instead of “”, so the preprocessor knows where to look

## Slide 14: Editing header files
If you do the following:
  Compile
  Edit a header file
  Do not edit any file that #includes it
  Compile
  the changes you made to the header file will have no effect
The OS keeps a timestamp of the last time files were edited
If the SOURCES are the same version as the compile, they are not recompiled
  This saves a ton of time when recompiling huge projects
  It also means that if the .c file isn’t recompiled, the header files are not re-included

## Slide 15: The Solution(s)
make clean before you make build
  Advantages:
    Catch-all solution (one step, always works)
  Disadvantages:
    It may take forever to recompile everything
Edit the .c files that include it, then undo, save, and compile
  Advantages:
    Way faster (usually)
  Disadvantages:
    Annoying to find all files that #include the header file in question
    Easy to forget one (which may not matter)

## Slide 16: Flicker

## Slide 17: How Display Works
The processor sets a location in memory
  A wire to the memory location sets the value
The screen gets its info from memory
  A wire to the memory location accesses the value
These two things cannot happen simultaneously
  If the screen refreshes ~60fps, and you write constantly, they will conflict often
If they conflict, who wins?
  The processor, 100% of the time
  Better for display to flicker than code to glitch unpredictably
You can’t change when the screen does its accessing
  That’s hardwired in
  Instead, change the when the code accesses the video

## Slide 18: Screen drawing order
Each pixel is drawn one-at-a-time
  Left-to-right, top-to-bottom
  ~60 Hz
Pauses shortly after each row
  HBlank
Pauses longly after the last row, then starts over
  Vblank
If we set pixels in the blank periods, there’s no way they will conflict with the video circuit
  As long as you finish setting in time

## Slide 19: Scanline
There is a register in memory that is incremented each time the screen finishes drawing a row. We call it the Scanline.
  When it finishes everything, it resets to 0
  Located at 0x4000006
#define SCANLINECOUNTER (*(volatile unsigned short *)0x4000006)
  0: drawing the first row
  159: drawing the last row
  160: beginning of vblank
  227: end of vblank
    Then it cycles back around.
Why volatile?
  Because it is changed by the hardware, C doesn’t expect it to change, so it only grabs it from memory once.
  Making it volatile tells C to grab it from the memory every time we tell it to